## Slide 1: Generating a Data-Driven Surrogate Model for Machine Damage Accumulation
Problem 1
Team name: What the Hack?
Bi Senior Foua, Madan Dahal, Laxmi Poudel

## Slide 2: PROBLEM DESCRIPTION
Sensor Data Analysis and Machine Learning
  Background
    Problem origination: Bernard M. Gordon Learning Factory but general to any machining shop
    Eventual Objective:
      Prognostics
      Remaining useful life analysis
      Predictive maintenance
      Forecasting
    Immediate Objective: Fault accumulation prediction
  Data
    Two weeks of labeled data for training
    5 machines: 3X Bridgeport, 1X Drill press, and 1X Lathe
  Challenges:
    Data cleaning
Sensor dataset
Training and Testing Data
Output

## Slide 3: Approach
Why develop a surrogate model?
Problem domain: Application of sensor data in PM, Industrial IoT, Health monitoring, Stock price prediction
Most popular approach:
  Deep Learning are effective for prediction and regression
  CNN, RNN, LSTM, Autoencoders are some of the popular DL methods
  Long et al. even combined CNN and ANN with multi-filters neural network to improve the predicting ability of the model [Long et al., 2018]
  Namuduri et al. provides common us of ML methods to PM using sensor data [Namuduri et al., 2020]
Programming Language: Python
Framework : TensorFlow, Keras
Algorithm: SVM, DL, GB, Ensemble, RF, KNN, LR
  To provide end user flexibility to choose model that works for their objective
Problem Understanding
Literature Review
Data Cleaning
Model Building
Model Testing

## Slide 4: Results
Machine Name | Model Used X-Axial (R Square value) | Computational Time | Model Used Y-Radial (R Square value) | Computational Time
Bridgeport3 | LR = .8262 Knn = .8649 SVM = .7690 DT = .7693 RF = .8558 GB = .7929 Ensemble = .8612 NN = .8723 | 271 ms ± 54.2 ms per loop | LR = .9507 Knn = .9512 SVM = .9018 DT = .9055 RF = .96.27 GB = .9481 NN = .8912 Ensemble = .9710 | 1.82 s ± 207 ms per loop
Lathe | LR = .5030 SVM = .9155 DT = .9223 RF = .9718 GB = .9619 NN = . 9122 Ensemble = .8923 Knn = 0.9622 | 4.17 ms ± 656 µs per loop | LR = .7249 SVM = .8418 DT = .9323 RF = .9313 GB = .9453 NN = .8513 Ensemble = .9444 Knn = .9494 | 2.95 ms ± 123 µs per loop

## Slide 5: Results
Comparison of R-value for Bridgeport 3 (Y-radial axis)
Correlation table for Bridgeport 3

## Slide 6: Findings and Discussion
  Rather than using a single approach to solve the problem, we wanted to see how do different machine learning methods result in different R-value
  Use of different ML methods allow user to choose the model that works best for their eventual outcome whether it be prognosis, forecasting, etc.
  Each model performed differently on each machine as demonstrated by different R-value for different machines
  The deep learning and ensemble models performed better in general compared to the other ML models

## Slide 7: Closure & Insights
  Real life data are messy and require lot of pre-processing
  Any ML used is only as effective as the training data it is fed
  Feature engineering and Data Processing could help improve precision

## Slide 8: Thank you! Questions?